## Slide 1
Interdisciplinary project · Review 1
NAVI
Navigation Assistant for Visitor Interaction
An autonomous follow-me micro aerial vehicle
for outdoor campus wayfinding
SCOPE · SENSE · SMEC
Vellore Institute of Technology
Notes: One sentence: a drone that physically leads campus visitors to their destination. Review 1 covers problem, objectives, scope, outcomes and team roles.

## Slide 2
The problem
02
Visitors get lost on a large campus
First-time visitors to a large campus routinely get lost. Static signage assumes you already know the layout, and asking for directions depends on finding someone free to help.
01
Signage is passive
Boards show a map, not a route. Visitors must self-localise before they can use them.
02
Human guides do not scale
Staff and volunteers are finite, and demand spikes on event days.
03
Phone maps stop at the gate
Consumer navigation apps carry little internal campus pathway detail.
Why a drone
It removes the localisation step entirely.
The visitor does not read a map, orient themselves, or translate directions.
They follow something visible, moving and unambiguous.
An aerial guide is unobstructed by crowds, parked vehicles and ground clutter.
Notes: Frame the pain first, then justify the aerial approach.

## Slide 3
Related work
03
The campus already has a wayfinder
VIT Chennai operates an official 2D/3D interactive navigator at chennaiwayfinder.vit.ac.in.
What it does well
A complete, maintained database of campus buildings and facilities
Detailed 3D geometry and search across academic, hostel and facility categories
Accessible from any browser, already known to the campus community
The gap it leaves
A map still requires the visitor to work out where they currently are
They must then translate a route on screen into what they see around them
This is precisely the self-localisation step that NAVI removes
NAVI is complementary, not a replacement. The wayfinder's destination database is a natural data source for our route graph, and we are in the process of requesting it.
Notes: Raise this before the panel does. Acknowledging existing work and explaining the gap is far stronger than being caught unaware of it.

## Slide 4
Disciplines
04
Why this is a multidisciplinary problem
No single discipline can deliver a drone that safely leads a human being across a live campus.
Mechanical
Airframe integration, propulsion, vibration isolation, weight and thrust budget.
Electronics & Comm.
RTK GNSS correction link, telemetry, sensor integration, power distribution.
Computer Science
Route graph, path planning, MAVLink mission logic, pacing controller, web interface.
Human Factors
How a stranger reads a flying guide: pacing, lead distance, arrival cues, trust.
Safety & Regulation
Geofencing, failsafe design, risk assessment for shared campus roads.
Survey & Mapping
Pathway and road surveying, junction geo-referencing, overhead obstruction logging.
Notes: Safety and human factors are not add-ons; they constrain the engineering.

## Slide 5
Problem statement
05
To design and demonstrate an autonomous micro aerial vehicle that receives a destination from a campus visitor, plans a route over a geo-referenced map of campus roads and pathways, and physically leads that visitor to the destination at walking pace while maintaining safe separation from people and traffic.
Not solved by
GPS navigation apps, which lack internal campus pathway data and still require self-localisation.
Core challenge
Coupling an autonomous aerial vehicle to the unpredictable pace of a walking human.
Success looks like
A visitor with no prior knowledge reaches an unfamiliar building without asking anyone.
Notes: Read the statement aloud once. The novelty is the human-pacing coupling, not the drone.

## Slide 6
Objectives
06
Objectives
Five objectives, each independently demonstrable.
O1
Survey and model the campus
Build a geo-referenced graph of campus roads and pathways using RTK GNSS, including per-segment altitude constraints and launch pad siting.
O2
Achieve autonomous waypoint flight
Fly a planned route between any two nodes using shortest-path planning, with centimetre-level RTK positioning.
O3
Implement human-paced leading
Maintain a configurable lead distance ahead of the visitor, adapting speed and holding position when they stop.
O4
Build a visitor-facing interface
Allow a guest to select a destination and share position from their own phone, with no app installation.
O5
Establish a safety envelope
Define and test geofencing, altitude floor, return-to-launch, low-battery and guest-lost failsafes.
Notes: Five objectives, each independently demonstrable. O1 to O3 alone constitute a complete deliverable.

## Slide 7
Visitor experience
07
How it works, from the visitor's side
1
Arrive
Visitor reaches the campus gate and finds the kiosk.
2
Select
Chooses a destination on the touchscreen, scans a QR code.
3
Share
Phone browser asks permission and begins sharing position. No app to install.
4
Follow
Drone launches, holds a lead ahead, and paces to the visitor's walking speed.
5
Arrive
Drone signals arrival at the building and returns to the launch point.
No installation required
Position sharing uses the browser Geolocation API on a page served from the ground station, so the visitor needs only a phone and a browser. This removes the largest adoption barrier for a guest who is on campus once.
Notes: Walk the panel through this as a story before showing any architecture. Step 4 is highlighted because it is the technical contribution.

## Slide 8
Architecture
08
System architecture
Visitor phone
Destination choice and live
position over the browser
Geolocation API
Ground station
Route planning over the
campus graph; RTK base
streams corrections
Companion computer
Mission logic and pacing
controller; talks MAVLink to
the flight controller
Pixhawk
Executes position targets,
stabilisation and all
failsafes
Key design decision
Phone GPS, not onboard vision
Re-identifying one pedestrian from altitude is an open research problem. Phone GPS is accurate to a few metres, which is sufficient for pacing.
Key design decision
Altitude set per segment
Cruise height comes from the surveyed worst overhead obstruction on each segment, not one campus-wide value.
Notes: Expect a question on why not computer vision. The phone-GPS answer converts a research problem into an engineering one.

## Slide 9
Route graph
09
The campus route graph
Every flight path is composed only of segments the team has surveyed on foot.
Main gate
Lab block
Planned route
Other surveyed segments
What is stored
Node — a surveyed point: junction, entrance or bend, with RTK coordinates.
Edge — a walkable connection, storing length, minimum safe altitude and surface type.
Planner — Dijkstra over the graph, penalising road surfaces so verge routes are preferred.
Launch pad — a surveyed take-off and landing point; routes are composed of legs between pads.
Every route is pre-generated and human-inspected before it is ever flown.
Notes: This slide answers 'how do you guarantee it will not fly somewhere unexpected'. The drone can only ever compose surveyed segments, and a whitelist check rejects any waypoint not in the graph.

## Slide 10
Endurance
10
Endurance sets the leg limit
The maximum guided distance is derived from measured flight time, not chosen arbitrarily.
~8 min
S500 flight time with payload
0.8 m/s
design walking speed
350 m
maximum leg length
Why 0.8 m/s
The primary users are visiting parents and guests, not students. Typical adult walking speed falls with age, and designing to a median would leave roughly half of them short of battery mid-route. We size the endurance budget for the slower walker, so a typical visitor simply arrives with reserve to spare.
Longer routes: staged legs
Destinations beyond 350 m are reached by chaining legs between surveyed launch pads, with a battery swap at each handoff. Total guided distance is therefore bounded by pad placement rather than by battery capacity, and coverage extends by adding a pad rather than by changing the aircraft.
Notes: The eight-minute figure is an estimate until the packs are capacity-tested with the SkyRC BD250. Say so if asked; do not quote it as measured.

## Slide 11
Contribution
11
What is actually new here
Autonomous waypoint flight is a solved problem, and we use it off the shelf. The contribution lies elsewhere.
01
Human pacing
Coupling an autonomous aerial vehicle to the unpredictable speed of a walking person, including stop, lag and loss recovery.
02
Surveyed altitude model
Per-segment cruise height derived from logged overhead cabling and canopy, rather than a single campus-wide number.
03
Zero-install guidance
The visitor is guided using only their existing phone browser, removing the adoption barrier of a dedicated app.
Notes: Have this ready for the inevitable 'what is novel' question. Conceding that the flight stack is off-the-shelf makes the real claim more credible, not less.

## Slide 12
Scope
12
Scope
In scope
Outdoor flight over surveyed campus roads and pathways
Guided legs of at most 350 m, sized for a 0.8 m/s walking speed
A fixed set of pre-mapped destinations, every route pre-generated and inspected
One visitor, or one small group, guided at a time
Daytime operation in fair weather, below a defined wind threshold
Longer routes staged across surveyed launch pads with battery swaps
Fully autonomous flight under ADAPT institutional clearance
No flight directly over occupied vehicles or live traffic lanes
Out of scope
Indoor navigation and building interiors
Beyond-visual-line-of-sight operation
Multiple simultaneous guided visitors
Night flight and adverse weather
Autonomous charging docks with precision landing
Carrying luggage or any payload for the visitor
Live obstacle detection and dynamic re-routing in flight
Notes: A tightly bounded scope is a strength at Review 1. Be ready to defend each exclusion on safety or feasibility grounds.

## Slide 13
Safety
13
Safety envelope and failsafes
Every condition has a defined action, and each is tested deliberately rather than assumed.
Condition
Action
RTK fix lost beyond timeout
Hold position, then return to launch
Telemetry link lost
Return to launch
Visitor position stale beyond 30 s
Hold position, then return to launch
Battery below reserve
Return to launch immediately
Geofence breach
Stop and hold
Design principles
The safe default is always to hold, then return — never to continue on stale data.
Waypoints are whitelisted: any target not matching a surveyed node is rejected before upload.
Routing prefers verges and open ground over carriageway wherever an alternative exists.
Notes: Reviewers respond well to a failure table. It shows the team has thought past the happy path.

## Slide 14
Resources
14
Existing laboratory inventory
No significant procurement required. All primary hardware is available in the ADAPT laboratory (AB3-710).
Airframe
S500 quadcopter with Pixhawk 2.4.8, or X500 V2 build kit
Positioning
Helical H-RTK F9P base and rover pair; Here4 multiband RTK GNSS
Compute
Pixhawk 6X + Jetson Orin NX bundle; Raspberry Pi 5 as alternative
Perception
Intel RealSense D455 depth camera; SIYI A8 gimbal with object tracking
Communication
SiK telemetry 915 MHz; Skydroid T12 / H12 control link
Power
Multiple LiPo packs, SkyRC charger, discharger and battery analyser
Visitor interface
Raspberry Pi 7" touchscreen for the gate kiosk
Procurement is limited to propeller guards and consumables. Campus flight clearance is granted for all campus coverage, and the project operates under ADAPT's existing registration.
Notes: Emphasise that the project is not blocked on purchasing, and that the RTK hardware is what makes the outdoor approach viable.

## Slide 15
Progress
15
Software developed so far
Two working applications, both running on placeholder data pending the RTK survey.
Visitor kiosk
Runs on the gate touchscreen
Destination search and selection
Dijkstra routing over the campus graph
Automatic splitting into legs at the 350 m limit
Walking distance and time shown at 0.8 m/s
Generates the waypoint mission for the ground station
Mission control dashboard
Runs on the ground station
Waypoint planning: place, drag, reorder, set altitude and speed
Route distance, duration, altitude range and battery estimate
Restricted and no-fly zone conflict detection along each leg
Flight simulation with live telemetry and flown trail
Telemetry abstraction ready for a MAVLink provider
Notes: Demonstrating working software at Review 1 is unusual and worth showing. Be clear that the campus data is placeholder until the survey is complete.

## Slide 16
Team
16
Team roles and contributions
Five members across three schools: Mechanical (SMEC), Electronics (SENSE) and Computer Science (SCOPE).
Carollo Aradhan V
26BMH1173 SMEC, Mechanical
Flight platform lead
Airframe assembly and integration, propulsion and payload mounting, vibration isolation, weight and thrust budget.
Utkarsh Dilipkumar Ghorpade
26BEC1215 SENSE, Electronics
Positioning and electronics lead
RTK base and rover setup, correction link, telemetry, sensor integration, power distribution.
N Arun
26BCE1550 SCOPE, Computer Science
Autonomy and flight software lead
MAVLink mission scripting, companion computer integration, pacing controller, failsafe logic.
Muhammed Farhan
26BCE1551 SCOPE, Computer Science
Mapping and path planning lead
Campus route graph, RTK survey data processing, shortest-path planner, per-segment altitude model.
Sayanjeet Das
26BCE5502 SCOPE, Computer Science
Interface and validation lead
Visitor web interface and kiosk, destination database, guided trials, documentation and reporting.
Notes: If asked why three members are from Computer Science: the software workload splits cleanly into flight autonomy, mapping and planning, and the visitor-facing system.

## Slide 17
Deliverables
17
Expected outcomes
01
Geo-referenced campus map
A surveyed graph of roads and pathways with RTK-logged coordinates, per-segment altitude limits and sited launch pads, reusable by other projects.
02
Working autonomous guide
A drone that flies a pre-inspected route from the gate kiosk to a selected building without manual input.
03
Human-paced leading demo
Demonstrated lead-distance maintenance, hold-on-stop, and recovery when the visitor falls behind.
04
Safety and failsafe report
Documented geofence, altitude floor, return-to-launch and battery-reserve behaviour, with test evidence.
05
Zero-install visitor interface
A phone-accessible destination picker and position share requiring no app.
06
Technical documentation
System architecture, wiring, configuration and operating procedure for reproducibility.
Notes: The campus map and safety report have value independent of whether the full leading demo succeeds.

## Slide 18
Plan
18
Work plan and verification gates
Each phase must pass its gate before the next begins.
Phase 1
Survey and mapping
RTK walkthrough of roads and pathways; build and validate the graph.
Gate
Graph covers every destination; pads sited so no leg exceeds 350 m.
Phase 2
Autonomous waypoint flight
Node-to-node routes flown on command, open ground, no visitor.
Gate
Stable hover, then repeatable route flight without intervention.
Phase 3
Human-paced leading
Integrate visitor position; tune lead distance and hold behaviour.
Gate
Pacing validated in simulation before any live flight.
Phase 4
Interface and validation
Kiosk and web page, failsafe testing, guided trials.
Gate
Every failsafe triggered deliberately and observed.
Notes: Gates matter more than dates at Review 1. They show the team knows what 'done' means for each phase.

## Slide 19
Risk
19
Identified risks and mitigation
Risk
Mitigation
Endurance
Roughly ten minutes of flight limits route length.
Map short routes; stage battery swaps between guided runs.
RTK fix loss
Signal degrades near tall blocks and dense canopy.
Log fix quality per segment during the survey; route around dead zones.
Overhead obstructions
Cabling and tree canopy above road corridors.
Record every span during survey; set cruise altitude per segment.
Traffic below
Campus roads carry vehicles and two-wheelers.
Route over verges and open ground; never over live lanes.
Wind sensitivity
Slow lead flight is the worst case for an S500.
Characterise position-hold error against wind; set an operating threshold.
Phone position noise
Handset GPS varies by device and sky view.
Measure the error distribution; apply filtering and threshold hysteresis.
Regulatory clearance is not listed as a risk: campus flight permission is granted and the project operates under ADAPT's existing registration.
Notes: Naming risks unprompted is what separates a Review 1 that lands from one that gets picked apart.

## Slide 20
Thank you
NAVI · Navigation Assistant for Visitor Interaction
Questions and feedback welcome
20
Notes: Close by restating the single-sentence version of the project and invite questions on scope.